# Text boxes

Applications

- APCO25 compatible video link

- UAV/UGV/AUV long range narrow band links

- Wireless Video to/from Troops/combat in urban areas and caves.

- Long range, non-line-of-sight, digital encrypted video communications.

- Electronic News Gathering (ENG)

##### 344 Coogan Way, El Cajon, CA 92020, PH 619-401-1967 Fax 619-401-1971 www.avalonrf.com

DESCRIPTION

The TR438ST is a rugged eight antenna UHF space-time digital, encrypted, software defined transceiver intended for demanding long range, non-line-of-sight, high mobility, wireless live video applications over narrow band channels without link breakup. 

The TR438ST tunes from 460MHz to 960MHz in 200KHz increments. It has an output power of 8W over a 3db bandwidth of 161KHz, a gross data rate of 1.1Mbit/sec & Turbo FEC with an 80% payload. It supports both QAM and OFDM modulations with the addition of space-time equalizers

to improve signal to noise ratio and eliminate Doppler effects in high speed mobile applications. 

The TR438ST transceiver offers the following channels:
a)	Two video channels with adjustable bit rates and VITC/watermarking.
b)	One audio channel with one talk-back audio channel.
c)	One two way, half-duplex, digital encrypted communications channel. 	
d) 	Alarm channel.
e) 	Four analog telemetry channels.

# FEATURES

- ”All in one” low latency digital transceiver: Video, audio, data, command & control, telemetry and alarm over a 900Kbit/sec net data rate.

- MPEG2/MPEG4 encoding/decoding with low latency.

- FIPS140-2/FIPS197 encryption (AES) with 128 to 256 bit keys.

- Turbo F.E.C. (802.16 compatible) with 80% payload.

- Software Defined Radio(SDR): Supports both QAM and ODFM modulations.

- Tunes from 460MHz to 960MHz in 200KHz channels (2500 channels).

- RF out=8W. RF input sensitivity is –102db for a BER of 1E-6.

	Remote control of the receiver via a RS232 channel.

## TR438ST	PRELIMINARY

#### Eight Antenna UHF Space-Time Transceiver