TR430-2G 1W Wireless Digital Link

# Text boxes

Other OEM Applications:

Wireless RS232 link

Wireless audio link

Wireless alarm link

Wireless telemetry link

Wireless remote control

Interoperability systems

Remote analog to RS232 and vice versa

### 344 Coogan Way, El Cajon, CA 92020, PH 619-401-1967 Fax 619-401-1971 www.avalonrf.com

DESCRIPTION

The TX430-2G is a 1W secure, robust, digital wireless two-way link for OEM use. It is miniature, light weight and low power.

Operating frequency: UHF from 460MHz to 960MHz, offering over 700 channels at the same location.

Smart automatic control: Remote on/off and gain control. RF frequency synthesizing and power control.

KISS design: Only manual control is an On/Off switch.

# TR430-2G Features

- RS232 at 1.2K-200Kbaud, half duplex

- Daisy chain IIS interface

- One two way audio channel to G.729 with acoustic echo and noise cancellation.

- Remote On/Off via receiver

- Radio section
RF output of 30dbm (1W)
RF input sensitivity of –99dbm
Includes Forward Error Correction (FEC) =>
Range urban area: 1000 feet non-line-of-sight
Range open space: Four miles line-of-sight

- Power consumption: 3.3V/950mA in transmit mode

## TR430-2G Optional features

- TCP/IP and USB interfaces

- Video link (with Module A)

- Voice cancellation

- FIPS140-2/FIPS197 Encryption

- GPS option

- Alarm I/O option

- Two analog telemetry inputs and outputs, each with 10 bit resolution and a 500Hz sampling rate