|  | MODEL: SV-1700-HB Datasheet 17.0” Sunlight Readable LCD Monitor 1,300 Nits (Cd/m2) HIGH BRIGHTNESS NEMA 4 or 4X Sealed Front Panel Stainless Steel #304, brushed 17.0" Active Display Area Adjustable Brightness Controls 1280 x 1024 resolution (Autosync. to VGA) Digital controls w/on screen display Custom OEM Designs Available |
| --- | --- |
| StealthVU High Brightness, Sunlight Readable Monitors The StealthVU-HB series of monitors are powerful sunlight readable displays that are designed to operate in extreme ambient light conditions. StealthVU-HB monitors outperform commercially available products that wash out in direct and indirect sunlight conditions. Ideal for outside use in marine/mobile, interactive kiosks or display advertising applications. StealthVU monitors are “Plug & Play” compatible with no drivers to load. Stealth has developed a wide range of products to fit your exact application needs. Available in NEMA 4 /4X Stainless Steel, Panel/Rack mount and Open Frame configurations. MODEL SIZE 17" MODEL # SV-1700-HB Environmental STANDARD: NEMA 4X Front Panel protection against windblown dust and rain, splashing water, hose-directed water and corrosion Screen Size 17.0" (Diagonal) Type TFT Active Matrix Liquid Crystal Controls Rear Exit, Left (-), Right (+), Up, Down, Proceed, Reset, Power and LED Indicator Brightness 1300 cd/m² (nits) (adjustable) Controls On-Screen Display Brightness, Contrast, Auto Adjust, Image Position, Image Adjust, Color Adjust, Display Mode, Language Select, OSM Lockout, OSM Time-out Colors Analog Input: 16.7 million Dimensions (W x H x D) Panel Mount: 18.94"(W) x 17.0"(H) x 4"(D) Rack Mount: - 19.0"(W) x 15.75"(H) x 4"(D) OEM Chassis - Call Factory for Dimensions Response <30ms Typical Unit Weight Unit 18 lbs (8.16 Kgs) approx Contrast Ratio 300:1 Operating Temperature 32 to 104° F ( 0 to 40° C ) Humidity 30% ~ 80%, non-condensing Altitude Sea Level to 12,000 ft. Viewing Angle (typical) 50° / 60° (Horz.) Left / Right 40° / 60° (Vert.) Up / Down Shipping/Storage Temperature -14° to 140°F (-10 to 60°C) Humidity 10% to 90%, non-condensing Altitude Sea Level to 53,000 ft. Viewable Image Size Horizontal: 13.3" / 337.92 mm Vertical: 10.6” / 270.34 mm Panel Finish Stainless Steel Type 304, #4 Finish (brushed) Resolutions Supported Auto Sync. from 640 x 480 to 1280 x 1024 Warranty 1 Year Parts & Labor Native Mode 1280 x 1024 Options OEM Custom Designs Custom Paint Video Signal ANALOG: 0.7 Vp-p/75 Ohms NTSC, S-Video, PAL Sync Signal Separate sync: TTL level (Positive/Negative) Signal Cables 15 pin to 15 pin D-sub cable, detachable Connector Type Analog 15 Pin D-Sub RCA, Y/C Power Input 12VDC Power Input External Power Supply Universal Power Suppy (removable) 90-240V, +12VDC@100W Protective Shield Anti-Reflective Tempered Glass Overlay Touchscreen (optional) STANDARD: RESISTIVE OPTIONAL: CAPACITIVE, & SAW NOTE: Specifications subject to change without notice. |