CONTACT:  	André Rebelo

Extech Global Public Relations Manager

+1.781.434.3901

andre.rebelo@extech.com

Extech EX845 METERLiNK™ Clamp Meter Transmit Readings to FLIR IR Cameras
Increased connectivity accelerates IR inspections and diagnostics

(Waltham, MA, USA) Extech Instruments (www.extech.com/instruments), makers of the best handheld test and measurement tools, introduces the new EX845, a 1000A AC/DC CAT IV clamp meter with new METERLiNK™ technology and a built-in infrared thermometer.

Introducing METERLiNK™
METERLiNK™ is an exclusive new technology that wirelessly connects FLIR infrared cameras to Extech meters via Bluetooth™ to accelerate and simplify inspections. During infrared inspections of electrical components, users can transmit key electrical readings such as current or voltage from an Extech EX845 clamp meter directly to a FLIR infrared camera. METERLiNK™ instantly imprints the electrical readings onto a related infrared image not only adding time-savings, but also ensuring accurate, coordinated documentation for PdM inspection reports.

About the EX845

The rugged new Extech EX845 1000A clamp meter is designed to deliver safety and versatility—without compromising performance or innovation. The EX845’s advanced True RMS meter functions include AC/DC current, voltage, resistance, capacitance, frequency, infrared and contact temperature, diode-test, and continuity check. The fast-responding EX845’s peak hold function captures inrush currents and transients.

The bright 4-digit, 4,000 count backlit display is complemented by several one-button functions including data hold, min/max, and selectable auto- or manual-ranging. The large 1.7" (43mm) jaw opening handles conductors up to 750MCM or multiple conductors such as two 500MCM. For quick, point and shoot temperature readings, the patented, non-contact IR thermometer with laser pointer is useful for fast hot-spot detection.

The EX845 has a CAT IV-600V, CAT III-1000V overvoltage safety rating and is CE and ETL approved. The meter comes complete with an 8-piece professional test lead set, a 9V battery, Type K temperature probe, and a belt holster. NIST certification is available for this product. To learn more about the new EX845, or to find an Extech distributor, please visit www.extech.com/instruments.

About Extech Instruments
Extech Instruments is recognized as the source for the best handheld test and measurement tools worldwide. Founded in 1971, Extech is known for its depth and breadth of innovative testers and meters suited for electrical, HVAC, building/restoration, as well as a host of environmental testers for measurement of sound, light, humidity and other factors. All Extech meters are distributed worldwide through leading representatives, distributors and OEMs. The company is headquartered in Waltham, Massachusetts, USA and is ISO 9001 2000 certified. Extech is a wholly owned subsidiary of FLIR Systems, Inc.

###

Attention Publishers: 
Please send all sales leads to Tracy Milhomme, Marketing Communications Coordinator,

Extech Instruments, 285 Bear Hill Rd., Waltham, MA  02451 USA
Phone: 781-890-7440; Fax: 781-890-7864
Email: tracy.milhomme@extech.com

# Specifications

﻿	 		Range 				Basic Accuracy

AC/DC Current 	0.1 to 1000A 			±2.8%

AC/DC Voltage 	0.1mV to 1000V 		AC: ±1.5%; DC: ±2.8%

Resistance 		0.1 to 40MΩ 			±1.5%

Capacitance 		0.001nF to 40,000μF 		±3.0%

Frequency 		0.001kHz to 4kHz 		±1.5%

IR Temperature 	-58 to 518ºF (-50 to 270ºC) 	±2.0% rdg or ±4ºF/±2ºC

Type K Temperature 	-4 to 1400ºF (-20 to 760ºC) 	±(3%rdg+9°F/5ºC)

Continuity 		Yes

Inrush 			Yes

Diode 			Yes

Dimensions/Weight 	10.6x4.3x2" (270x110x50mm)/ 13.6oz (386g)

# Text boxes

Extech EX845 Highlights:

- 1000A AC/DC Clamp

- True RMS, Autoranging

- Built-in infrared thermometer

- METERLiNK™ connectivity to FLIR IR cameras

- Peak, Hold, Max./Min. data functions

- Captures inrush and transients

- Thermocouple temperature

- 1.7” (400mm) jaw opening