FOR APPROVAL ONLY				CONTACT:	John Bell

prseitz@bellsouth.net

954-970-3394

Specialized Products Company Introduces

Low Cost Fiber Optic Visual Fault Locator Tools

SOUTHLAKE, TX—SEPTEMBER XX, 2010—An economical laser-optimized fiber optic visual fault locator enabling technicians to quickly and easily diagnose and troubleshoot fiber cable damage has been introduced by Specialized Products Company (SPC).

Available in two product selections—the VFL-680 and VFL-640— the SPCfiber Low Cost Visual Fault Locators feature a bright 650-nm laser light to ensure fast and easy location of loss points in fiber optic patch cords, patch panel and enclosures.  The rugged, lightweight Visual Fault Finders, which quickly locate sharp bends and breaks, also feature battery life up to 30 hours in continuous mode and 40 hours in modulated mode.

The VFL-680 features a 2.5mm universal adapter for FC/ST/SC while the VFL-640 offers a 1.25mm universal adapter for LC/MU connectors.

VFL-680 and VFL-640 Key Features:

• Compact, ergonomic design for ultimate portability

• Visible wavelength is 630 nM – 680 nM

• High-powered fiber optic laser with Output power: Singlemode

fiber > 0.3mW, Multimode fiber > 1.0mW

• Illumination: Class III A laser diode

• Operation method: Continuous illumination

• Connector interface 2.5 mm for ST, FC/PC and SC

Connector interface 1.25 mm for LC/MU

• Battery: 1.5V 2 each AA (included)

• Size; Length: 162+- 2mm

• Size; Diameter: 16.5 mm

• Includes professional storage case

These Fiber Optic Visual Fault Locators—the VFL-680 and VFL-640— are immediately available online at: http://www.specialized.net/Specialized/Content/Visual_Fault_Locator_VFL640_VFL680.aspx.

Based in Southlake, Texas, SPC offers a comprehensive selection of over 10,000 off-the-shelf tool, test and tool kit solutions for field service engineers, technicians, professional integrators and installers.

About Specialized Products Company

Since 1965, Specialized Products Company, www.specialized.net, has supplied service professionals with tools, over 100 customizable industry-specific tool kits, shipping cases and test equipment.  The company’s personalized assistance and same-day shipping covers over 10,000 competitively priced installation, field service and repair solutions.

--30—