PRESS RELEASE

For Immediate Release

Sierra’s New Cryogenic InnovaMass® Vortex Flow Meter Offers Advanced Liquid Gas Measurement

Monterey, CA — August 16, 2012 — Sierra Instruments today introduces a new cryogenic version of its InnovaMass® 240 multivariable mass vortex flow meter for advanced, more reliable measurement of liquefied gases, including liquid nitrogen, liquid oxygen, liquefied natural gas (LNG), liquefied petroleum gas (LPG), down to -330°F (-200°C).

Historically gauged by inexact turbine flow meters, liquid gas flow can now be calculated with precision using Sierra’s new flowmeter. The InnovaMass also contains no moving parts that will wear out or require service, an added advantage that provides stable readings and an increased service life.

The new InnovaMass cryogenic version has undergone extensive testing and field validation over the last several years, proving that the meter is preferred versus traditional turbine meters for measuring mass flow rates of cryogenic fluids down to -330°F (-200°C). Using a special cryogenic temperature RTD, mass calculations are done with the latest density equations of state for liquid oxygen, nitrogen, argon and carbon dioxide.

The InnovaMass 240 can be loop powered with power in, a programmable analog output and a HART or MODBUS signal riding on the same two wires.

To learn more about Sierra’s InnovaMass, visit https://www.sierrainstruments.com/products/cryo.html  or contact us to request a quote.

-MORE-

ABOUT SIERRA

A global leader in flow measurement and control for over 40 years, Sierra instruments designs and manufactures high performance flow instrumentation for gas, liquid and steam applications commonly found in the pharmaceutical, scientific research, health, energy and semi-conductor industries. With over 150 offices in 50 countries, Sierra is uniquely positioned to provide their innovative products and lifetime support for the leading companies of today and the growth enterprises of tomorrow.

Press Contact

USA:

Maryadine Washington

Marketing Communications Manager

800.866.0200 x108

m_washington@sierrainstruments.com

Barbara Oud

European Marketing Coordinator

b_oud@sierrainstruments.nl