Press Contact: 	Kelly LaBarre

PH: 860-793-4333

kelly.labarre@GemsSensors.com

Intrinsically Safe Pressure Transmitters Meet CSA Demands

Plainville CT, February 2013: Gems Sensors & Controls announces the introduction of the 31CS and 32CS Series intrinsically safe pressure transmitters. These series have been approved by CSA to the standards required for both USA and Canadian use in hazardous areas. The two new Series are identical, with the exception of the pressure diaphragm. 32CS Series transmitters feature a thicker diaphragm and a pressure restrictor to withstand the rigors of cavitation or extreme pressure spikes, improving stability and reliability in pulsating applications.

Based on the successful Gems 3100 & 3200 Series products, when used with a zener barrier the CS Series transmitters are certified for operation in the following areas:

Class I, Division 1, Groups C and D

Class I, Zone 0 Ex ia IIB T4 Ga

Class I, Zone 0 AEx ia IIB T4 Ga

Applications include hazardous area installations, such as wellhead automation, gas distribution and gas compressors. 31CS/32CS transmitters are compact and durable in harsh outdoor environments. They may be directly fitted to pipe work, so require none of the small bore pipe work needed to remotely utilize non-Division 1 certified transmitters. This enables 31CS/32CS Series transmitters to reduce time and cost of installation.

Both the 31CS and 32CS Series feature proven Sputtered Thin Film sensing technology, 17-4 PH stainless steel wetted parts, and ASIC-controlled thermal compensation and signal conditioning. They are available in a wide variety of factory-configured settings, or may be configured to the customers application needs. Exceptional long-term stability (0.2% full scale/year drift) and high accuracy (0.25% full scale) together with high resistance to shock and vibration makes this product ideal for demanding applications.

About Gems Sensors & Controls

Founded in 1955, Gems is a preferred supplier to thousands of OEM companies across a broad range of industries through out the world due to its extensive application knowledge, innovative sensor and miniature solenoid valve designs, and customer centric approach to problem solving to meet customer-specific needs. Gems Sensors & Controls is a leading global manufacturer of: liquid level, flow, and pressure sensors; solid-state relays and barriers; liquid and pneumatic miniature solenoid valves; and pre-assembled fluidic systems with facilities in North America, Europe, and Asia. Gems Sensors & Controls is ISO 9001, ISO 13485, UL, and CE certified.

For more product information, contact Gems Sensors & Controls, One Cowles Road, Plainville, Connecticut 06062. Phone: (800) 378-1600. www.GemsSensors.com.

### SHAPE  SHAPE  SHAPE