Press Contact: 	Kelly LaBarre

Phone: 860-793-4333

kelly.labarre@GemsSensors.com

Gems Sensors & Controls Announces the Launch of the 3500 Series Pressure Transducer

February 4, 2014: New 3500 Series pressure transducers follow on from the highly successful 3100 and 3200 series transducers from Gems, bringing a versatile low pressure capability to the product line and opening up a host of new applications across medical and general industrial markets.

Available in 7 pressure ranges from 0-1 bar (0-14.5 PSI) to 0-16 bar (0-232 PSI), the 3500 series is characterized by its compact size, absolute, compound and gauge reference capability and its ability to operate over a wide temperature range of -40°C to + 125°C (-40°F to 257°F), which offers flexibility for a host of applications.

Proven MEMS technology provides high levels of performance and stability. Standard units have an accuracy of 0.25% full scale. The transducer is designed for more than 100 million FS cycles, with a long term drift of just 0.2% FS/year eliminating the need for costly recalibration. Less than 45 mm long (1.77 inches) and weighing just 35 g (1.23oz), the compact construction of 3500 Series transducers make them ideal for installation where space is at a premium. 316L stainless steel wetted parts and an all welded construction make them highly compatible to harsh chemicals and environments.

Voltage and Current outputs are available with a range of electrical connections and pressure ports to choose from making the 3500 extremely versatile and suitable for many applications without modification.

More complete specifications, dimensions and wiring diagrams for this sensor and other Gems pressure transducers are available at GemsSensors.com.

About Gems Sensors & Controls

Founded in 1955, Gems is a preferred supplier to thousands of OEM companies across a broad range of industries through out the world due to its extensive application knowledge, innovative sensor and miniature solenoid valve designs, and customer centric approach to problem solving to meet customer-specific needs. Gems Sensors & Controls is a leading global manufacturer of: liquid level, flow, and pressure sensors; solid-state relays and barriers; liquid and pneumatic miniature solenoid valves; and pre-assembled fluidic systems with facilities in North America, Europe, and Asia.  Gems Sensors & Controls is ISO 9000 Registered, has UL Approvals, and provides CE Marking for applicable products. .

For more product information, contact Gems Sensors & Controls, One Cowles Road, Plainville, Connecticut 06062. Phone: (800) 378-1600. www.GemsSensors.com.

###