Press Contact: 	Kelly LaBarre

Phone: 860-793-4333

kelly.labarre@GemsSensors.com

Gems Sensors & Controls Introduces CSA Approved Explosion Proof Pressure Transducers

Plainville, CT: Now available from Gems Sensors & Controls are the 31EP and 32EP Explosion Proof pressure transducers. Building on decades of pressure sensor experience, the latest versions are approved by CSA for use in hazardous areas. Applications include hazardous area installations, such as artificial lift, chemical injection, and CNG compressors. 31EP/32EP Series transducers are compact and durable allowing them to be utilized in space constrained harsh environments

Based on the successful Gems 3100 & 3200 Series products, EP Series transducers are certified for operation in the following areas:

- Class I Division 1, Groups A, B, C and  D

- Class I Zone1 Ex d IIC T4 Gb

- Class I, Zone 1 A Ex d IIC T4 Gb

The two new series are identical, with the exception of the pressure diaphragm. The 32EP Series transducers feature a thicker diaphragm and a pressure restrictor to withstand the rigors of cavitation or extreme pressure spikes, improving stability and reliability in pulsating pressure applications.

Both the 31EP and 32EP Series feature proven Sputtered Thin Film sensing technology, 17-4 PH stainless steel wetted parts, and ASIC-controlled thermal compensation and signal conditioning. They are available in a wide variety of standard factory-configured settings, or can be configured to the customer’s specific application needs. Electrical connection can be directly threaded into installed electrical conduit pipe work, and a range of pressure fittings are available to simplify connection to process fluids. This enables 31EP/32EP Series transducers to reduce time and cost of installation.

Superior long-term stability ( 0.2% full scale/year drift ), higher accuracy (0.25% full scale) together with high resistance to shock and vibration makes this product reliable and dependable in demanding Oil and Gas applications.

For more information about the 31EP/32EP Series, and other Gems Sensors & Controls products, go to GemsSensors.com.

About Gems Sensors & Controls

Founded in 1955, Gems is a preferred supplier to thousands of OEM companies across a broad range of industries throughout the world due to its extensive application knowledge, innovative sensor and miniature solenoid valve designs, and customer centric approach to problem solving to meet customer-specific needs. Gems Sensors & Controls is a leading global manufacturer of: liquid level, flow, and pressure sensors; solid-state relays and barriers; liquid and pneumatic miniature solenoid valves; and pre-assembled fluidic systems with facilities in North America, Europe, and Asia.  Gems Sensors & Controls is ISO 9000 Registered, UL and CSA recognized, and provides CE Marking for applicable products as required.

For more product information, contact Gems Sensors & Controls, One Cowles Road, Plainville, Connecticut 06062. Phone: (800) 378-1600 or   www.GemsSensors.com.

###